MODBUS NETWORK INFO
Hardware: RS232 over serial to Arduino /dev/ttyACM0
Baud rate: 9600

- Broadcast: address 00
- Arduino: address 01
BEHAVIOR DEFINITION.
Protocol: Modbus RTU

MODBUS COMAND IMPLEMENTATION

- All communication is expected to be initiated by the server.
- When a node is given a command, it responds with a dataframe containing its -own- address. Master doesn't have an address.
DATAFRAME STRUCTURE - modbus ASCII

Name	Start	Address	Function	Data	LRC	End
Length (bytes)	2	4	4	4n	4	4
Desc	Colon ':' ASCII 3A	Station Address	Function code	Data	Checksum	CR/LF / 0D 0A

Maximum dataframe length: 256 Bytes

INTERACTIONS:

Request: please read back holding registers
Node Address
Code 03
2 bytes Starting register
2 bytes number of registers
CRC16

Response:
Node Address
Code 03
2 bytes Data length
Data
CRC16

Request: please change holding register NN
Node Address
Code 06
Register Address
Data contents

Request: please loop back
Code 08
Sub-function 00 00
Data field (two 16-bit words)
CRC Check

Example: 01 08 00 00 A5 37 DA 8D

Expected response:

ARDUINO MODBUS REGISTERS

INPUT REGISTERS
- Input registers are read-only, provided by IO devices. 16 bit.
- 00 : NTC0
- 01: PRT0
- 02: PRT1
- 03: Speed Feedback from
HOLDING REGISTERS
- Holding registers are for settings. 16 bit.
- 00: Speed request